## Slide 1
Q1.
Offset = 12bits 🡪 block size = 2^12 bytes =4KB (B即bytes)
Index = 10bits 🡪 2^10 = 1024 blocks
Direct mapped (講義P.34)
Total bits = 1024 blocks * (1bit valid + 42bits tag + 4096*8 bits data)
Data bits = 1024 blocks * (4096*8 bits data)
Ans = (43+4096*8)/4096*8 =1.00131 ~ =1.00
4.
Hit : valid + tag (P.44) [tag的63-32都是0]
Offset不重要
0x 1fffff48 = 1111111 1111111111 111101001000 🡪 valid = 0 , miss 一開始什麼都沒有
0x 1fffff50 = 1111111 1111111111 111101010000 🡪 valid = 1 , hit (tag也相同)
0x 1fffff58 = 1111111 1111111111 111101011000 🡪 valid = 1 , hit (tag相同)
0x 10034dc4 = 1000000 0000110100 110111000100 🡪 valid = 0 , miss 一開始什麼都沒有
0x 0ffe744c = 0111111 1111100111 010001001100 🡪 valid = 0 , miss 一開始什麼都沒有
0x10034db4 = 1000000 0000110100 110110110100 🡪 valid = 1 , hit(tag 也相同) (第4次已經有抓了)
~
0x10034dac = 略 🡪只有做後3bit(2進位就是12bit相同，因此一定是hit)
0x10033ee4 = 1000000 0000110011 111011100100 🡪 valid = 0 , miss 一開始什麼都沒有
0x3004d978 = 11000000 0001001101 100101111000 🡪 valid = 0, miss 一開始什麼都沒有
Hit rate =5/10 = 50%

## Slide 2
Q2
Read BW (Miss in I$ + read miss in D$ + write miss in D$)
Write-allocate will make a read request to RAM when write miss.(意思是write miss要做read時是取64bytes)
假設有1000個ins，則
Miss in I$ = 1000*0.3% =3
read miss in D$ = 250*2% = 5
write miss in D$ = 100*2% = 2
Total bytes = 5+2+3 = 10個data = 10*64 =640bytes
1000 ins , CPI = 2 🡪 2000 cycle
Ans : BW = 640/2000 =0.32
2. Write BW ( write miss in D$)+write hit in D$)
Write-through only write a word(4 bytes) when write (意思是要做write時是取4bytes)
一樣1000ins ,
write miss in D$ = 100*2% =2
Write hit in D$ = 100*98% =98
Total bytes =(2+98)*4 = 400bytes (只要是write 不管是miss之後要write還是hit要write都是4bytes)
400 / 2000 = 0.2

## Slide 3
Q3.1 Cache P.78
the CPI for the processor in the table using only a 1-level cache.
Miss penalty = 100ns/0.5ns = 200 cycles
CPI = 1.5+1*7%*200 = 15.5
2. CPI = 1.5+1*7%*400 = 29.5
3. the CPI for the processor in the table using a 2-level direct-mapped cache.
CPI = 1.5+1*7%*12 (L1 cache miss 、 L2 cache hit)+1*7%*3.5%*200 (L1、L2 both miss)
= 2.83
4. CPI = 1.5+1*7%*12 (L1 cache miss 、 L2 cache hit)+1*7%*3.5%*400 (L1、L2 both miss)
= 3.32
5. the CPI for the processor in the table using a 2-level 8-way set associative cache
CPI = 1.5+1*7%*28 (L1 cache miss 、 L2 cache hit)+1*7%*1.5%*200 (L1、L2 both miss)
= 3.67
6. CPI = 1.5+1*7%*28 (L1 cache miss 、 L2 cache hit)+1*7%*1.5%*400 (L1、L2 both miss)
= 3.88

## Slide 4
Q3.2
3-level
CPI = 1.5+1*7%*12 (L1 cache miss 、 L2 cache hit)+1*7%*3.5%*50 (L1、L2 miss、L3 hit)
+ 1*7%*3.5%*1.3%*200 (L1 L2 L3 all miss)
= 2.468~=2.47

## Slide 5
Q4 .two-way set associative cache with four 4-byte blocks (Cache P.55)，本題沒說給的是blk add，因此我認位有包含offset
1.4byte blocks 🡪 offset = 2bits (2^2 = 4)
2. two-way set(代表一個set2個blk)+總共four blk 🡪 set num = 2 🡪index 1 bits
tag ind offset
0(0000000) 🡪 tag = 0 , ind = 0
1(0000001) 🡪 tag = 0 , ind = 0
2(0000010) 🡪 tag = 0 , ind = 0
3(0000011) 🡪 tag = 0 , ind = 0
4(0000100) 🡪 tag = 0 , ind = 1
5(0000101) 🡪 tag = 0 , ind = 1
6(0000110) 🡪 tag = 0 , ind = 1
7(0000111) 🡪 tag = 0 , ind = 1
### set –ass的方式時，index bits數是看set num
講義P.73
本題因為不會出現replace的狀況，因此與LFU或是MRU無關
0(0000000) 🡪 tag = 0 , ind = 0 一開始啥都沒有 miss , 因此在set0裡的其中一個block 會搬mem(0)~mem(3)
1(0000001) 🡪 tag = 0 , ind = 0 , hit 因為0的時後搬過了
2(0000010) 🡪 tag = 0 , ind = 0 , hit 因為0的時後搬過了
3(0000011) 🡪 tag = 0 , ind = 0 , hit 因為0的時後搬過了
4(0000100) 🡪 tag = 0 , ind = 1 ,一開始啥都沒有 miss , 因此在set1(1/2=1)裡的其中一個block 會搬mem(0)~mem(3)
5(0000101) 🡪 tag = 0 , ind = 1 , hit 因為1的時後搬過了
6(0000110) 🡪 tag = 0 , ind = 1 , hit 因為1的時後搬過了
7(0000111) 🡪 tag = 0 , ind = 1 ,hit 因為1的時後搬過了
後面就都搬過了，全部都hit

## Slide 6
Q5(Vm )
P.21
Page size = 8KB 🡪 page offset = 13bits (2^13 = 8K)
19bits for virtual page number
Page table size = (2^19)*4bytes =0.5M*4bytes = 2MB
5 process : 2*5 = 10MB
P.30
2. Virtual page number = 19
1st = 256 blocks = 2^8 🡪p1 =8
p2 = 19-8 = 11
Page table size for 2nd levael= (2^11)*4bytes =8Kbytes
又因為1st table有256個entries(blocks)代表2nd table有256個

## Slide 7
題目說five applications that each utilize half of the virtual memory available
代表5個apllication 一個會用掉256/2 = 128個 2nd-level page table
因此minimum = 5 * 128 *8kB = 5MB (也就是不同apllication可以共用相同的1st page table，例如app1用前128個entry app2用後128個)
maximiun = 5*256*8kB =10GB (也就是雖然一個app只用到128個entry但是無法公用，因此每個app還是需要花256個)
3.
算1st level大小(照上面的想法)
Minumum (公用): 5*128*6bytes = 3840bytes
Maximin (不共用) : 5*256*6bytes = 7680bytes 🡪 題目要這ㄍ 我也不知道位啥QQ

## Slide 8
Q6
Page size = 4KB =2^12
N = 43-12 = 31
2. Page table size = 2^31*4bytes = 8GB